## Slide 1
Wireless remote temperature & humidity logger
Design side note
Up to 10 wireless remote sensors.
Temperature and humidity measurement.
Standalone long term data logging (Onboard SD writer)
PC connectivity (USB Data talker)
Feature

## Slide 2: Block diagram
Transmitter
Sensor
(DHT-22)
Transmitter
(RF315-TX-5)
MCU
(PIC16F1827)
DC-DC
(HT7733A)
2x AAA
Battery
SW & LED
Receiver
(RF315-RXB12)
MCU
(PIC18F4550)
LCD
(DMG12864i)
SD Card
SW&LED&BZ
Receiver
Power
Data
315MHz ASK
3.3V

## Slide 3: Radio TRX module study
Upper(CH1): RX module output Lower(CH2): TX module input
Bit rate survey

## Slide 4
Data frame design
Preamble
SFD
Payload
Sum
ID
Batt volt
Temp
Humidity
Preamble: [10101010]n
SFD: 10101011
Payload (Manchester encoded) Sum (Manchester encoded)
4bit
4bit
12bit
12bit
1
4
1
n
…10101010
10101011
Preamble
SFD
1
1
0
1
0
1
0
0
Payload, Sum (Manchester encoded)
SFD: Start Frame Delimiter
 | width | LSB | Offset | Range
ID | 4 | 1 | 0 | 0 – 15
Batt volt | 4 | 0.1 V | 1.6V | 1.6 – 3.1V (for 2 cells)
Temp | 12 | 0.1℃ | 0℃ | Signed 12bit
Humidity | 12 | 0.1% | 0% | Unsigned 12bit
…
…

## Slide 5
Outline of data frame recovery
INT2
TMR3
Remks:
1.Wait for data slicer leveling.
- Duty 50% is ideal for leveling.
- TMR3 is cleared by INT2 invoked by data rising.
- Count up preamble bit if period is good.
2.Bit rate detection.
- After counting enough bit, data slicer leveling is
expected to be stable.
- TMR3 is cleared by INT2 as well.
- Use TMR3 value to determine bit rate
3.Start synchronous data sampling.
- Once bit rate is detected, following data is sampled
by TMR3 INT.
- Each bit is poked twice to know 10 or 01 (or 11)
4.Start bit found.
- DATA “11” indicates start of payload.
5.Payload, Sum
- Data is from Manchester decoder.
Remks
1
2
3
TMR3INT
DATA
10
10
11
Start bit
N
N
Y
PAYLOAD/SUM Data
10
0
Noise
Data
01
1
Preamble + SFD
Carrier
*
*Carrier (w/o modulation):
for Quick Rx AGC stability
4
5
Bit rate
0
MAX

## Slide 6
TRX data waveform
Tx data
AGC
CTH
Rx data

## Slide 7
Xmit timing (data multiplexing)
sample
sample
sample
xmit
xmit
Sleep1
Sleep2
Sleep1
Sleep2
Ts(approx 60s)
Tx wait (sleep1) may vary randomly to avoid continuous data collision with other xmitters.
Ts

## Slide 8
RX PIC oscillator configuration
Figure from datasheet
8MHz
Xtal
1
48MHz
96MHz
1
48MHz
48MHz
48MHz

## Slide 9
RX PIC timer configuration
Timer | Width | Prescaler max | Tmax (@48MHz) | Used for
Timer0 | 16 | 1/256 | 1.4 s | Periodical interrupt (software tick)
Timer1 | 16 | 1/8 | 43.7ms | Not used
Timer2 | 8 | 1/16 | 0.341ms | PWM (Backlight brightness, Piezo Beeper) Prescalser (@SD card Initialization)
Timer3 | 16 | 1/8 | 43.7ms | Rx data sample clock

## Slide 10
Timer0 16bit periodical interrupt
0
0
1/16
18750 count  25ms
Timer configuration:
T08BIT  0 select 16bit width T0CS  0 select int clock T0PS2::0  3 select 1/16 prescaler PSA  0 use prescaler
12MHz
75000Hz

## Slide 11
Timer2 (SD Initialization, PWM backlight and beeper)
PWM for Backlight and beeper
12MHz
PWM Period = [(PR2)+1] x 4 x Tosc x Prescaler
At SD initialization
100-400kHz SPI clock is required.
Timer configuration:
T2CKPS  0 1/1 scaler PR2  30 Freq = 12M / 30 = 400kHz
Timer configuration:
T2CKPS  2 1/16 scaler PR2  255
Freq = 12M / 16 / 256 = 2.93kHz (minimum frequency)

## Slide 12
Timer3 Data sampling
12MHz
0
Select 1/8
1

## Slide 13
RX PIC Interrupts
1.INT2 (RX signal invocation)
2.TMR3 (RX signal sampling)
3.TMR0 (25ms periodical tick. Main system cycle)

## Slide 14: RX layout
5
4.3
2.0
80
115
USB
ICSP
ANT
SD
LCD
Push-sw

## Slide 15
10
10
10
7
80
76
8
7.6
7.5
18
7.6
10.4
5
6.3
6
7.5
4
68
92
80
113
Case Takachi YM-115
SW EXT PCB
RX layout cont.

## Slide 16: PCB design
Using EAGLE
Receiver 76 x 100mm
Transmitter 31 x 100mm

## Slide 17
RX software stack
USB-CDC
Using
Microchip application lib
USB serial
Dot matrix LCD
GLCD
Using picfun.com
Tiny FAT16
Original
Data receiver
Original
Application
Original
http://www.aitendo.com/product/2607